## Slide 1: The Risk to Space: Cybersecurity in the New High Ground
Scott Lynch
Senior Engineer, Security Onion Solutions

## Slide 2: Who am I?
Scott Lynch
Scott.Lynch@SLTekSystems.com
Twitter/LinkedIn @PacketEngineer
SANS Certified Instructor/Prior Author
SEC555: SIEM with Tactical Analytics
Senior Engineer, Security Onion Solutions
Founder/CEO, SLTek Systems
25+ Years in the Space Industry
Cisco Instructor/Adjunct Professor BCCC
US Navy Veteran, Electronic Warfare/IFO
GCDA, GDSA, GCIH, GNFA, CCNP-S, CCAI

## Slide 3: Our Reliance on Space
"From the moment we wake up to the instant we drift off to sleep, our daily lives are intricately woven with the threads of space systems, highlighting the indispensable role these celestial technologies play in shaping the tapestry of human existence on our Pale Blue Dot.“
-ChatGPT 2023
Notes: Cyberattacks on Satellites An Underestimated Political Threat
https://www.lse.ac.uk/ideas/projects/space-policy/publications/Cyberattacks-on-Satellites

## Slide 4: Satellite and Wireless Together

## Slide 5: Snapshot of the SATCOM Industry
Market value estimated at 200.3 billion USD in 2025 expected to grow
Commercial Space Growth
Massive Small Sat Constellations
The Moon and beyond
5G Use in Space
  NB 5G-IoT satellite communications
Notes: TOTUM https://totum.global/solution/
ROCKETLAB https://www.rocketlabusa.com/
ASTROSCALE https://astroscale.com/
RelativitySpace https://www.relativityspace.com/
SPACEX Starship https://www.spacex.com/vehicles/starship/
Planet https://www.planet.com/
NASA Artemis https://www.nasa.gov/specials/artemis/
SATELIOT https://sateliot.space/en/
https://spacenews.com/op-ed-nb-5g-iot-is-the-next-big-thing-in-the-space-industry/
https://www.mordorintelligence.com/industry-reports/global-satellite-communication-market

## Slide 6: Innovation in Space
Rapid Growth
  Failing forward Fast
Lowering the barrier to entry
  Building, Launching and Operating spacecraft
Move to cloud
  The push to Software as a Service (SaaS) solutions
IoT In Space
    NASA's IoT Lab
    Sateliot
Pushing the boundaries of Commercial off the shelf Technology (COTS)
Adoption of Minimum Viable Product (MVP)

## Slide 7: Typical Satellite communications Ground Station

## Slide 8: Typical Ground Station to Customer Architecture
Customer connects to ground station via terrestrial network of ISPs to ground station controller's network of ground stations
Ground station is configured with correct uplink/downlink parameters and pointing information to receive signals by ground station controllers
Telemetry and Commands routed back to customer via ground station terrestrial network

## Slide 9: Ground Station Terminals, Antennas and Equipment
Viasat Ground terminals
Viasat 13.5m Ka-band Broadband Gateway Earth Station Antenna
South Point Station, Hawaii
Typical radio rack
Satcom receiver

## Slide 10: Legacy Satcom Ground Station Equipment
Purpose built
Solid state
Mechanical
Upgradeable but at hardware level
Usually controlled over serial

## Slide 11: Cloud Based Ground Stations
https://aws.amazon.com/ground-station/

## Slide 12: Software Defined Radio (SDR)
“A radio communication system where components that have been traditionally implemented in analog hardware (e.g., mixers, filters, amplifiers, modulators/demodulators, detectors, etc.) are instead implemented by means of software on a personal computer or embedded system”
https://en.wikipedia.org/wiki/Software-defined_radio

## Slide 13: Software-Defined Satellites
SDR in Space
GEO to start LEO to follow
5G increased usage and deployment
  Connect massive numbers of Internet of Things (IoT) sensors and devices
  Voice & Data services for commercial, protected, and secure communications anywhere.
LEO to benefit
IP in Space
Lockheed Martin’s nanosatellite bus, the LM 50
Notes: https://satelliteprome.com/news/operators/satellite/software-defined-satellites-shaping-the-future-of-communications/
https://www.satellitetoday.com/innovation/2019/03/21/lockheed-martin-accelerates-transition-to-software-defined-space/

## Slide 14: Study: Eavesdropping on Internal Networks via Unencrypted Satellites
https://satcom.sysnet.ucsd.edu/
Consumer-grade satellite dish on the roof of a university building in San Diego, California
Positioning motor for the antenna
Consumer-grade TV tuner card to capture raw bytes.
Scanned for all transponders (position and frequency)
Used custom protocol-parsing code to reconstruct network packets.
Observed 411 transponders across 39 GEO satellites, and our single fixed-location dish could receive IP traffic from 14% of all global Ku-band satellites.

## Slide 15: Eavesdropping on Internal Networks via Unencrypted Satellites – Cont.
https://satcom.sysnet.ucsd.edu/
Cellular Backhaul
Unencrypted calls, SMS
End user Internet traffic
Hardware IDs (e.g. IMSI)
Cellular communication encryption keys.
Military and Government
Unencrypted VoIP
Internet traffic
Encrypted internal communications from ships, traffic for military
Detailed tracking data for coastal vessel surveillance
Police force operations
In‑flight Wi‑Fi
Unprotected passenger Internet traffic destined for in-flight Wi-Fi
Passenger web browsing (DNS lookups and HTTPS traffic)
Encrypted pilot flight‑information systems
In‑flight entertainment.
VoIP
Multiple VoIP providers were using unencrypted satellite backhaul, exposing
  Unencrypted call audio
  End user metadata
Internal Commercial Networks
Retail, financial, and banking companies all used unencrypted satellite communications for their internal networks.
Observed unencrypted
  Login credentials
  Corporate emails
  Inventory records
  ATM networking information.
Critical Infrastructure
Power utility companies and oil and gas pipelines used GEO satellite links to support remotely operated SCADA infrastructure and power grid repair tickets.

## Slide 16: What if we lost access?
Communication
  voice, data, and video services across the US and the world.
Navigation (GPS)
  Aviation
  Maritime
  Ground-based navigation,
    Emergency services
    Agriculture
    Surveying and mapping
  Cellular Communications
Financial services
  Financial transactions
  Stock trading
  Point of Sales Systems (POS)
Weather Forecasting
Television and Radio Broadcasting
Space Exploration

## Slide 17: Threats and Risks
Nation State Actors
Supply Chain
Software/Hardware Vulnerabilities
Cyber Attack
Denial of Service
Hacktivism
Ransomware
Physical Attack
Threats to Remote Sensing Satellites ACCRES Briefing
Notes: https://www.nesdis.noaa.gov/s3/2022-08/1.%20ACCRES%20-%20Space%20ISAC%20Brief.pdf

## Slide 18: Cyber Intrusion or Breach – Examples from NASA
2014 - JPL discovered a cyber intruder was able to upload malware to a server supporting JPL astronomical missions and research after a web-based program installed by the system’s administrator allowed the public to upload and execute files on the server.
  Investigation of the compromise revealed the administrator failed to update the software in a timely manner, providing the attacker an opportunity for unauthorized access via a JPL computer
2016 – A website misconfiguration resulted in an anonymous user gaining elevated privileges that enabled an individual to execute codes on a server used for software architecture development.
  The use of Secure Sockets Layer, which ensures that all data transmitted between the web server and browser remains encrypted, prevented JPL’s network security monitoring tools from identifying the actions taken by the bad actor prior to detection.
2011 - JPL discovered Chinese-based IP addresses in which cyber intruders gained full access to 18 servers supporting key JPL missions, including the DSN and Advanced Spaceborne Thermal Emission and Reflection Radiometer mission, and sensitive user accounts
  With full system access, the intruders were able to: (1) copy, modify, or delete sensitive files; (2) add, modify, or delete user accounts for mission-critical JPL systems; (3) upload hacking tools to steal user credentials and compromise other NASA systems; and (4) modify system logs to conceal their actions. Intruders resided within the system for 2 weeks before being detected and analysis of intrusion detection system log files revealed 87 gigabytes of data had been uploaded to the attackers’ IP addresses
2009 - A cyberattacker successfully penetrated a computer system at JPL and extracted approximately 22 gigabytes of program data by illegally transferring the information to an Internet Protocol (IP) address in China.
  The stolen data included information protected under International Traffic in Arms Regulations and Export Administration Regulations (ITAR)
2017 - A JPL server that runs source code used in ground operations for scientific spacecraft was compromised by foreign hackers who exploited a flaw in the software, hardware, or firmware that was previously unknown to JPL.
  As a result, the intruders remotely executed a code on the server without authentication. After gaining access to the server, the hackers were able to upload, manipulate, and execute various files and commands unrelated to controlling spacecraft.
Notes: https://oig.nasa.gov/docs/IG-19-022.pdf

## Slide 19: Chinese Accused of Interference of Two Satellites
Events occurred in 2007/2008
Moments of “interference”
Chinese threat actors blamed
During the final hack ‘the responsible party achieved all steps required to command the satellite’, but did not do so.
Terra
Landsat-7
Notes: Terra https://www.nasa.gov/mission_pages/terra/spacecraft/index.html
Landsat-7 https://landsat.gsfc.nasa.gov/satellites/landsat-7/
https://www.dailymail.co.uk/news/article-2062755/Real-life-Star-Wars-Were-Chinese-hackers-attacks-U-S-military-satellites.html
https://www.theguardian.com/technology/2011/oct/27/chinese-hacking-us-satellites-suspected

## Slide 20: Supply Chain Attacks and Risk
Notes: A History of Software Supply Chain Attacks https://www.sonatype.com/resources/vulnerability-timeline
GhostSec Targeting Satellite Receivers https://blog.cyble.com/2023/03/27/ghostsec-targeting-satellite-receivers/
OTORIO reveals GhostSec hacktivist group now targets Iranian ICS in support of Hijab protests https://industrialcyber.co/news/otorio-reveals-ghostsec-hacktivist-group-now-targets-iranian-ics-in-support-of-hijab-protests/
Dragos’ third quarter data says ransomware continues as one of most threatening financial and operational risks to industrial organizations
https://industrialcyber.co/ransomware/dragos-third-quarter-data-says-ransomware-continues-as-one-of-most-threatening-financial-and-operational-risks-to-industrial-organizations/
GhostSec hackers target satellite receivers, as threats toward satellite communication networks gradually rise
https://industrialcyber.co/threat-landscape/ghostsec-hackers-target-satellite-receivers-as-threats-toward-satellite-communication-networks-gradually-rise/
The Growing Risk of a Major Satellite Cyber Attack https://interactive.satellitetoday.com/the-growing-risk-of-a-major-satellite-cyber-attack/

## Slide 21: ViaSat Cyber Attack prior to Russia/Ukraine War
Russian hacking group Fancy Bear/APT 28
Infiltrated Satcom Provider ViaSat
Attacker exploited Skylogic's VPN appliance
Remote access to KA-SAT's network management segment
Overwrote key data in the flash memory on the SurfBeam modems
10k Viasat modems
https://cyberscoop.com/apt28-fancy-bear-satellite/
On the 24th of February, the KA-Sat satellite network was disrupted across several countries in Europe due to a cyber attack, leading to an interruption of broadband services for some customers (including some bigblu customers) on the network.
Notes: https://www.satellitetoday.com/cybersecurity/2022/04/11/experts-say-viasat-cyber-attacks-exposed-ground-terminal-satellite-supply-chain-vulnerabilities/

## Slide 22: Could This Happen Again?
Mebromi
Hacking Team UEFI Rootkit
Equation Group and Vault 7 Leaks
LoJax
MosaicRegressor
Trickbot
FinSpy
Especter
MoonBounce
CosmicStrand
BlackLotus
Notes: https://eclypsium.com/blog/endpoint-firmware-attack-timeline-introduction/
https://securelist.com/moonbounce-the-dark-side-of-uefi-firmware/105468/
https://www.reuters.com/article/us-china-cyber-moonlighters-idUSKCN1UX1JE
https://securelist.com/moonbounce-the-dark-side-of-uefi-firmware/105468/

## Slide 23: GPS Jamming
Reports of massive GPS interference along the Ukraine-Belarus border.
The activity was detected just north of Chernobyl, within the Chernobyl Exclusion Zone
Hawkeye 360, said on March 4, calling it a demonstration of the
“integration of electronic warfare tactics into Russian military operation to further degrade Ukraine’s ability for self-defense”.

## Slide 24: Electronic Warfare
Uplink
Downlink
Signal Spillage and Intercept
Spacecraft Fingerprinting
Three Modes of EW
  Electronic Attack (EA)
  Electronic Protect (EP)
  Electronic Support (ES)
Electronic Warfare (The US Defense Intelligence Agency)
Notes: https://m.koreaherald.com/view.php?ud=20220413000743\
https://www.ausa.org/sites/default/files/publications/LWP-115-Satellite-and-Ground-Communication-Systems-Space-and-Electronic-Warfare-Threats-to-the-United-States-Army.pdf

## Slide 25: Other Scenarios
Ransomware
Denial of Service
  Jamming Ground and Satellite
Hacktivism
Physical Attacks
  Power, Terrestrial ISP’s and ground infrastructure
Insider Threat

## Slide 26: Protection Starting Points
Implement Zero Trust and Segmentation
End to End Encryption
Monitoring, Monitoring, Monitoring …
Physical Security
Forensics and Incident Response (IR) Capabilities
Awareness Training
Tabletop Exercises and Planning for Breaches
Audits and Risk Assessments

## Slide 27: Detection and Defense
Inventory of Hardware and Software Assets
  Document findings
Technical Debt
  Retire of End of Life (EOL) Operating Systems and Hardware
User Awareness Training
  Use your “Human IDS” to your benefit
Tripwires and Honeypots
  Low-cost, High Value Indicator with Detections
Centrally Collect and Analyze Logs
  Don’t just collect them, use them!!
Network Security Monitoring (NSM)
  Security Onion/Zeek

## Slide 28: T-Pot Deutsche Telekom Security GmbH
Notes: https://github.com/telekom-security/tpotce

## Slide 29: Security Onion
Notes: https://github.com/telekom-security/tpotce

## Slide 30: Government Support
CISA Advisory: Strengthening Cybersecurity of SATCOM Network Providers and Customers
Updated May 10, 2022: The U.S. government attributes this threat activity to Russian state-sponsored malicious cyber actors. Additional information may be found in a statement from the State Department.
Actions to Take Today:
• Use secure methods for authentication.
• Enforce principle of least privilege.
• Review trust relationships.
• Implement encryption.
• Ensure robust patching and system configuration audits.
• Monitor logs for suspicious activity.
• Ensure incident response, resilience, and continuity of operations plans are in place.
CISA Shields Up!
https://www.cisa.gov/news-events/cybersecurity-advisories/aa22-076a
Notes: https://www.cisa.gov/news-events/cybersecurity-advisories/aa22-076a
https://www.cisa.gov/shields-up

## Slide 31: SPACE ISAC 2019

## Slide 32
Notes: https://www.nesdis.noaa.gov/s3/2022-08/1.%20ACCRES%20-%20Space%20ISAC%20Brief.pdf

## Slide 33: The Future Defender…..Today
What kind of training would new space defenders need to be successful at protecting corporate and national assets?
Training
  Blue/Red a Mix of Both!
  Understanding your system is critical
  Knowledge Areas
  Programing/Scripting
  Cloud Technologies
  IoT Systems
  Software Defined Networks (SDN)
  Network Monitoring
  Forensics
  Incident Response

## Slide 34: Have Questions?
Scott.Lynch@slteksystems.com
LinkedIn @PacketEngineer
Twitter @PacketEngineer